# Welcome

## Joris Al, Managing Director of Research Institute for Transport (AVV)

## Brain center of transport knowledge

## Purpose is to improve traffic management  - m

## Discussing merger with another institute to combine efforts

## Would like share their knowledge with us

## Congestion is first and foremost in their minds and they are looking at a number of solutions to tackle the congestion problem

## In the middle of discussions for road pricing - 2012 is the anticipated date - need to begin implementation today

## Belgium is introducing a road vignette - different than what The Netherlands will be implementing

## Not far enough along to have a uniform type of road pricing in western Europe

## Trying to influence the user of the system by giving more information on congestion and alternative routes - one method of enhancing traffic management

## Looking at emerging in-car technologies to improve the vehicle as well as road safety

## Doing pretty well in road safety but could do better

### In-car systems

### Improvement of infrastructure

## The approach to their own infrastructure

### Infrastructure-oriented culture

### All these users that drive on the roads and make them deteriorate and unfortunately they have to maintain it at a cost of a lot of money

### This manner of looking at the infrastructure is obsolete

### Looking at a public-oriented service that is for the public

### Culture change that is very difficult

### Target for director general to be the most public-oriented public service by 2008

## International exchange of information is very important

## They are a member of the European Council for Transportation Research Institute (28 members)

### In many countries in Europe - the same research is being done in about 5-6 places

### International exchange of projects, new technologies, should be far more important on our agendas so that we can improve faster with less cost

## Would like to improve both the Dutch information and the U.S. information

## Exchange of information between the institutes

# Dynamic Traffic Management in the Netherlands, an Overview

## Frans Middelham - Senior Advisory, Road Infrastructure and Traffic Management, Ministry of Transport Public Works and Watermanagement - Transport Research Center (AVV)

## Main Presentation

### Inhabitants per square km - densely populated

### Economic activity is related to the road network - NS and EW road orientation

#### Northern portion appears to not have connections, but they do

### Contribution of transport to economy

#### 60-70% related to transport - including employment and other factors

### The Ministry of Transport, Public Works and Watermanagement

#### Minister

#### Secretary General

#### AVV is part of the Ministry

### Organization of the AVV

#### Headquarters

#### 9 regional directorates in charge of the regional road networks and water management

#### Much of the country is below sea water

#### 1953 there was a major flood that killed nearly 2000 people - storm  surge from the North Sea

#### Protect against the water

#### Deal with the traffic and the major roadways - all components

#### 6 specialist departments - some of which are being merged

#### Nearly 10,000 employees

### Main tasks

#### Project from flooding

#### Water management

#### Road network

#### Etc.

### Expenditure in transport sector in M€

### Problems

#### Congestion costs are 0.8 B€ per year

#### Accessibility of main ports

#### Threat to

##### Distribution function - critical location for some shipping

##### Jobs and economy

##### Environment

##### Safety

## Dynamic Traffic Management

### Special lane facilities and lane management

### Policy goals and objectives

#### Stronger economy by improving accessibility

#### Enabling traffic and transport growth

#### Reliable and predictable door to door accessibility

#### Innovation is a must

#### Rapid elimination of maintenance backlogs - large problem that generates congestion when underway

#### Road pricing necessary - very difficult for politicians

### Traffic Management as a Control Scheme

#### Traffic management and demand management are part of the scheme

#### Traffic management is a part of control

#### Giving signals to the road users is a critical component

##### Incident management

##### Intelligent transport systems

##### Dedicated lanes

##### In-vehicle information - believed to have an influence on mode choice

#### Different measures have different effects that vary by time

#### Road pricing is mainly effectively influencing mode choice / demand

#### Have several control systems

#### Other parties are capturing traffic data by means of GSM tracking of vehicles

### Dynamic traffic management

#### Motorway signaling

#### Ramp metering

#### Dynamic route information

#### Information measures

#### New developments

### Motorway Signaling Systems since 1981

#### Gantries every 500 m

#### Change speeds to control traffic flow

#### When everything is fine - all signals are blank

### Function of the system

#### Want to deliver a service to road users - close lanes for incidents or road works

#### Throughput

##### Increased by 4-5%

##### Average throughput without any incidents

##### Does not include the impact of crashes

#### Safety assessment (1983)

##### Increased stability of traffic streams

##### Overall decrease of accidents by 15-25%

##### Decrease of secondary accidents by 40-50%

##### Helps prevent congestion

#### Safety assessment (1996)

### In place since 1981

#### Total to date - 997.3 km

#### Planned - 61.0 km

### Ramp Metering since 1989

#### Use large signals

#### Use overhead signals

#### Put pressure on the road user that there is a signal on the ramp - typically they are up to normal speeds to get on the motorway

#### 4 signal heads - 2 overhead (facing the queue) and 2 ground mounted (facing the driver at the stop bar) for 2-lane ramp

#### Stop line and there are detectors

#### There is a bypass lane for emergency vehicles

#### For

##### Alleviate motorway congestion

##### Better merging

##### Discourage "rat running" - vehicle jumping of the motorway to avoid congestion and hop back on

#### Several assessment studies

##### Increase speed

##### Reduction of shockwaves

##### Capacity increase of 5%

##### Reduction of "rat runners"

##### Expecting a decrease in accidents

#### Total ramps - 44

#### Planned - 16

#### Not all ramps have a ramp meter

#### Recently the Minister noted a desire increase in ramp metering

#### Want to build a link between the scientific people and practice

#### Policy tends to come afterwards

#### First there is some technology/experience and then next comes the policy and politicians

#### Early Video w/o metering - vehicles tend to cross the painted gore area and leave the acceleration lane empty

#### W/metering - higher speeds, better merges

#### Vehicles stored on slip ramp prior to metering:  1500

#### Vehicles stored on slip ramp after metering:  800

#### Some have bus by-pass lanes

#### Typical length of slip-ramp is 300 m

#### Some ramp meters have cameras installed for photo enforcement

##### in the control cabinet there are facilities to incorporate a camera

##### not all ramps have a camera, though it may look like it does

##### public doesn't always know if there is or not a camera

##### fine for violating the meter is 150€.

### Dynamic Route Information Panels Since 1990

#### DMS gantries over the roadway

#### For

##### En route information to inform users about queues

##### Major incident information and response

#### Several assessment studies

##### Difficult to assess the impacts of traveler info

##### In normal conditions, 8-10% or drivers are reacting to the information and can have a major effect on operations - recurrent congestion

##### Drivers are more satisfied.  More comfort, less stress

#### Different implementations and tests

##### Queue length

##### Travel time

##### Graphical

#### Total implementation:  101

#### Planned:  22

#### This is a measure that will be less important in the future because of the information that will be available in the vehicle

#### By law it is not the ministry's job to give traveler information directly to the user - information is sold/provided to information providers who give it to users through various sources

### Tidal Flow Lane

#### Running from ??? To Amsterdam - 15 km

#### A lane that is reserved and operates in the peak period in the peak direction (to Amsterdam in the morning and out in the evening)

#### Decided in early 1992 to make it a carpool lane

#### When it was opened, it was opened as a carpool lane

#### Was also opened in a period when the government / cabinet was sent home and there was an interim minister of transport and he decided to create a carpool measure

#### Now a normal lane for all vehicles - no longer a carpool measure

#### Was only a carpool measure for 3-4 months

#### The load in the morning is too high

#### Minister at that time had the idea of alleviating congestion but the media

##### Phrasing was that they were fighting congestion rather than helping people avoid congestion

##### Key message of the media - that it cost a lot and the attitude of the Minister of "my way" or the highway - empty lane syndrome

##### Didn't make the organization behind it organized to get the lane utilized

##### Low utility compared with a huge cost

##### Major problem was that the communication with the public was very bad

##### Should have emphasized the benefits of the lane instead of getting into the business of defending yourself

##### One opinion is that they still do a bad job of this

##### Former minister was fined for using the lane with 1 occupant and he won in the legal system - there is no process in the legal system

### Rush-hour Lane (Hard Shoulder)

#### Use of the hard shoulder during rush hours

#### Several in operation and there is a large scheme to install more of them

#### Signaled with lane control signals

#### Discussion about how these lanes should be signaled

#### Plus Lane (small left lane, lower speed)

##### 2.7 m wide

##### only - no

##### Speed for all lanes - not just the plus lane

#### 70 km/h is the speed limit during the operation of the lane

#### Still discussion about what the speed should be

#### Normally speed is applied to the whole cross-section

#### When there are 2 cross-sections when there is a merging - there will be a lower speed limit on the congested road and a higher speed on the uncongested road

#### Standard lane width is 3.5 m but there are situations under normal conditions where it is smaller - this is a special lane that is only operated under special conditions

#### Standard shoulder width is 1.25 on the left and 3.0 meters on the right shoulder

#### Restriping of pavement from 2 lanes to 3 lanes and reduced it

#### For hard-shoulder running the width is 3.5 m

#### The variable speed limits are required when you implement hard shoulder running because of the safety issues

#### In the off-peak, the plus lane will have a red X and will not be used

#### Signs

##### 3 lane freeway

##### Width restrictions - allowed vehicle widths are placed on the signs in a red circle

##### Trucks are not allowed on the plus lanes (max width 2 m - no trucks)

### Plus Lane (small left lane, lower speed)

#### Safety considerations

#### Truck, plus, rush hour, and tidal flow lanes

##### Total implementation:  94.9 km

### Incident Management

#### Tow away trucks

#### Communication critical

### Monitoring Since 1995

#### Every 500 m every lane through the central part of the country with highly dense monitoring areas

### Traffic Management Centers

#### Motorway, control and signaling route information panels

#### Ramp metering

#### Tidal flow lanes

#### Truck lanes

### New Developments and Trials

#### New graphical signs

#### Use for road user surveys

#### Provide information and ask them about information presented

#### Road section speed control

##### Picture vehicle

##### Measure travel time

##### Measure distance and determine speed

##### Speeders get a ticket automatically

### Lane Departure Warning assistant - several trucks equipped

### Devices in the road surface to change the striping and delineation

### Framework for an ITS Architecture

#### Traffic management system

##### Structured vision of traffic management

##### Policy, measures, implementation

#### Traffic control architecture, etc.

#### Application architecture

#### Architecture of the technical

# Strategic Models

## Frank Hofman - Senior Advisor, Strategic Models and Forecasts, AVV

## What is a model?

### Base year

#### Types of traveler

#### Choice behavior for each type

#### Choice models

### Future year

#### Population

#### Changed choice situations

#### Forecast:  new travel behavior

## What roles do models play?

### Appraisal (before)

#### Models can be used to appraise policy options in advance (before implementation).

### Evaluation (after)

#### Models enable the impacts of policy measures to be isolated from other factors that affect mobility

## How reliable are models?

### Reliability depends on that of the data fed into it and the quality of the theory of behavior and the factors that affect that behavior

### Not crystal balls

### Intended as an aid to making well-founded decisions on different policy options in the here and now

### AVV Transport Research Centre ensures that models used are up to date

### AVV TRC expertise include awareness of the scope of the validity of the model

## The models in this presentation

### TIGRES XL - land-use interaction model; gives the effect in accessibility on land use and vice versa

### LMS - national model system; assess impacts of changes in land use on accessibility and assess changes in accessibility on land use

### ALBATROSS - takes into account space-time constraints; uses same input as LMS and the same measures that come out of the LMS; feed results of ALBATROSS back into LSM

### SMILE+ - freight model that takes impact of growth on freight demand; logistic trends; goods movement

### RGM - model that disaggregates results for lorries that come out of SMILE+ for both national and regional models -

### NRM - regional model system - one of the most important in the Netherlands

## LMS

### LMS stand for the National Model System for Traffic and Transport

### Make forecasts of mobility and the use of the main network and the rail network

### Strategic appraisal of different policy packages

### Global - large - scale model

### Complex because the contain a lot of choice dimensions; ownership / trip decision / mode and destination choice / time of day choice / route choice

### Four-stage model with sub models for driving license acquisition and car ownership

### All sub models use structures compatible with national individual (and household) decision making

### Highlight disaggregated including spatial characteristics

### Pivot point method accurate description of base year combined with growth factors

### Based on cross section data (1995)

### Structure

#### Tour frequencies

#### Mode and destination choices

#### Time of day choice

#### Assignment

#### Time/cost skims

### Random utility model

#### Don't use this for modeling of specific stretches of roadway - use regional model for that

#### Revealed preference data

#### Stated preference data

#### Pros and cons of both types of data

### Data

#### National trip survey

#### 60,000 households

#### 158,000 persons

#### 1308 destinations, 5 modes, 490 socioeconomic groups (age, car ownership, societal participation, sex, and income)

#### Attraction e.g., commuting:  employment

#### Purposes:  commuting, home based business, non home based business, education, shopping, other, education for children, and other for children

#### Nested logit model

### Commuting

#### Mode specific constants

#### Constant for intrazonal traffic

### Input and Output

#### Context scenarios relate to things such as

##### Number of inhabitants by gender and age

##### Number of households

##### Employment in each sector and total

#### Keep behavior constant - do not necessarily change the behavior according to generations (baby boomers vs. current elderly) - changes and variations are accounted for through ownership penetration and other factors

### Horizon of current white paper is 2020

### Scan the future further ahead to 2040 and sometimes even 2050

### Outcome may be forecast of mobility

#### number of trips made by mode type

#### Volumes on the network throughout the day

#### Composition of the traffic - pass cars vs. lorries

#### Travel times and speeds

#### Can use for cost benefit analysis

### Elasticities by Fuel Price

#### Vary according to literature

#### 0.27-0.31

### Major drivers of mobility

#### Spatial, demographics, and socioeconomic factors

#### Policy measures such as the building of infrastructure, better utilization of existing infrastructure, pricing policy, etc.

### Established in the 1980's

### Limitations

#### No forecasts of freight within this model - rather use an O-D matrix from a lorry-model and input it into this model

#### Strategic model for the whole country.  Not intended to produce findings for particular sections of road.  Used for estimating the impacts of a whole infrastructure building program.  Not for predicting the effect of specific rush hour lane

### Applications

#### National Traffic and transport Plan

#### Mobility Policy Document

#### Spatial Planning Policy Document

#### Various High Speed Line Studies

#### Cooperation on Accessibility

#### Etc.

### Validation of Model

#### Reasonably close so far

## NRM

### New Regional Model

### Designed to produce regional traffic forecasts

### Provide better understanding and information required to develop regional transport policy

### Used for carrying out planning, exploratory, and other studies

### A source of information on mobility in a region

### Based on same philosophy of LMS but on a regional scale

### Important for national and regional consistency

### AVV

#### \responsible for basic assumptions and development of model

#### Ensures transfer of knowledge to regional directorates

#### Coordinates all model applications

### Basic model for all regional exploratory and planning studies

### Provides basic info for variety of regional studies at the municipality level for example

### Incorporates context and policy issues

### Limitations - same as the national model system

#### Makes accurate predictions for national trunk roads and major connections but not for urban roads

### Uses

#### Indicators for a particular study area

#### Input into regional policy evaluation / cost-benefit analysis

#### Other uses

## NRM - one specific road project

## LMS - entire country

## When you do the national level modeling, do what's going on the neighboring countries impact the model?

### Estimate the growth of the cross-country traffic / use a growth factors to get it on the matrix

# Creative Solutions for Traffic Congestion:  the "Traffic Jam Reduction" Project

## Antoine de Kort, Senior Advisor, Economics and Freight Transport, Deputy Project Manager of FileProof

## Some of the early results from their revolutionary project taking place in the Dutch Ministry

## "FileProof" is the Dutch term - File means congestion

## Background and Context, Objectives

### Increase in road traffic

### 2% each year and will continue over the next 20 years

### Mobility Policy Document - long-term measures for mobility

### Road pricing not before 2012

### Mid-term measures (rush-hour lanes) delayed due to environmental issues

### Large-scale maintenance works, 2006/2007

### Ministry:  people don't want it any more

## Objectives

### Do everything within reach

### Experiments with visible effects on congestion

### First effects in 2006 and 2007, continued until 2012

### Any solution:  infrastructure, public transport, etc.

### First stage:  involvement entire Ministry

### Second state:  also activating external knowledge and creativity

### Approved ideas implemented in unaltered form

### Overall responsibility:  CEO Rijkswaterstaat

### Direct support:  Minister and Governmental Boards

### Stakeholders had opportunity to give feedback on how to reduce congestion

### Ideas received from entities were forwarded to the ministry in original form - no variation or modification was made

## Reducing Excessive Congestion on Local Scale

### Delay for any car user should be less than 10 minutes on a yearly average

### Objective is to remove a specific number of vehicles using any number of and combination of measures to reduce it

## The Traffic Jam Reduction Approach

### Act, don't talk! (phrase of the project)

### 14 Feb - employees to give ideas for solutions to traffic jam reduction - received over 2000 ideas in 2 weeks

### Independent expert team reviewed the ideas and gave them scores for various aspects such as term of realization and expected impact on congestion

### Identified 30 real projects that could be done in 2 years and have a real visible effect on congestion

### All selected by prime minister before 10 April

### Parliament was informed and project leaders were identified

### 20 April - 2nd stage

#### Ideas entered around 5 general themes

### Held creative sessions - including new ideas (750)

### 23 May - new series of projects/proposals

### Prime minister wants to present the list of projects when she presents her 2007 budget

## Overview of Initiated Projects

### Reducing regular congestion

#### Extended acceleration lanes

#### Continuous line on fast lanes near ramps - works to reduce weaving

#### New direction signs at intersections - helps prevent unnecessary movements - give information on lane drops, etc.

#### Extended exit lanes (German:  "Stauventil")

##### Fix exits that extend into the GP lanes - extend the hard shoulder pavement and allow storage at exit on them

##### Congestion is on the GP lanes and extend ramp upstream of the exit for additional storage

#### Coordinated ramp meters on Amsterdam Beitway (A10)

##### "green wave" expert team

##### Adjusted opening and closing times of bridges around peak hours

##### Traffic jam warning signs on local network - provides information when users have the opportunity to take an alternate route before they get on the motorway - needs to be a good alternative to work

#### reducing irregular congestion (incidents, maintenance, construction works)

##### Mobil barrier (tidal flow)

##### Slightly dented car?  Pull over elsewhere

##### Accident screens preventing congestion due to curiosity feature - mobile and have to be moved to the accident location - looking at newer ones that are much more easy to transport

##### Flashing lights off at incident site - disturbing to other drivers on the motorway - already a rule in country but it is not followed.

#### Seducing people to act differently

##### Modernized driver's education/exam

##### "free" public transport on trial

##### Regional commuter cycling routes - not of high quality and have to make improvements to make it mode attractive

##### Exemplary role ministry in teleworking

## Discussion

### Average commuter distance is about 10-15 km but increasing - almost at 20

### First project accomplished

#### Road surface cleaner

#### Device to remove fluids from the surface after an accident - use a porous asphalt shoulder material

### Accident screens - when used

#### Successful on opposing congestion

#### Difficult to install the barrier screens and takes lots of time before it is installed

#### Would recommend it because it benefits the congestion

### Licensing

#### One test to get license

#### No additional testing required

#### 20 hours of practice required for young people to get exam

### Plans for cost-benefit analysis of strategies

#### Proposals had to have a cost-benefit analysis

#### As part of each budget, the project has to estimate the cost before getting money

#### Evaluation process within the project team to evaluate the effects of the individual projects - they identified the locations where the projects would be implemented and then work to assess the impacts

### Safety impact of turning off safety lights at incident location

#### If there is a vehicle with its lights on, then it should be the one in the rear and not facing the opposing direction

#### Another advantage is that a great deal of the freeways have automatic congestion warning systems before you reach the incident

### Breakdown of congestion in recurring vs. nonrecurring congestion

#### They have statistics, but the vision from the Minister is that they are equally important

#### U.S. average is 50% but perhaps the estimate in The Netherlands is 70% recurring and 30% nonrecurring

### Simplicity of the process and ease of project selection

#### Would the Ministry think of repeating this process at some time in the future?

#### She requested the agency to do a third round and do this again, but they figure it is difficult to really come up with new ideas - perhaps need to involve a different group of people

### What motivated people to submit ideas?

#### Internally, it was the work as part of their job

#### The ones entered ideas which have been initiated have been contacted by the project manager with compliments from the Minister - gotten attention

# Ring Road Management

## Henri Stembord, Senior Advisor, AVV

## Ring road:  series of roads within town for orbital distribution

## Beltway:  motorway or freeway, originally enclosing the urban area

## Important function of getting local traffic into the city (Rotterdam)

## Compact driving

### High density of traffic

### Small lateral (and longitudinal) distances

### Possibility of an additional traffic lane

### Higher capacity

## Speeds limits

### Built-up areas - 50m/h (70 km/h) - 30 km/h - "at a footpace"

### Rural areas:  100 km/h - 80 km/h - 60 km/h

### Motorways (2350 km) - 120 km/h (1880 km - 80%) - 100 km/h (470 km - 20%)

### Various roads impacted by pollution

## Air Pollution and Traffic Operations

### The first 80 km/h section due to air pollution in 2002 - section in Rotterdam

### 10 additional hot spots 80 km/h examined in 2004 (some in Amsterdam, Rotterdam, Den Haag, Utrecht)

### 4 additional in 2005

### Deal with locational air pollution and not necessarily regional

#### Contribution to solving the air pollution problem

#### Not enough

#### Will increase and there are European regulations to consider and which impact the country

### Minister promised to study the possibilities and the effects of 80 km/h (100% enforcement) on the 4 Ring Roads - in combination with High Density Driving

## High Density Driving

### Infrastructure

#### Longitudinal

##### Road signs

##### VSL

##### Enforcement

##### Platooning

#### Lateral Direction

##### Plus & Peak Lanes

##### Reversible Lanes

##### Narrow Lanes (temporary)

##### Narrow Lanes (permanent)

### In- car

#### Longitudinal Direction

##### Cruise control

##### Advanced cruise control

##### Intelligent speed adaptation

##### Auto vehicle guidance

#### Lateral

##### Lane change assistant

##### Lateral distance control

##### Automated vehicle guidance

### Additional traffic lane

### So HDD - HDD + 1 (80 km/h; 100% enforcement)

### Issues:

#### Entire ring road?

#### All the time?

#### 80 km/h:  relation with air pollution, width of lanes

### Several Alternatives

#### Effects on environment, traffic safety, congestion, travel time, cost, and benefit-cost ratio

#### Reference 2010:  planned expansions are realized; 100 km/h everywhere except hot spots

#### 80 km/h on ring roads everywhere 24/7

#### 80 km/h everywhere 24/7 and HDD everywhere

#### 24/7 is expensive in terms of vehicle hours of delay

#### HDD expensive because of construction cost

### 2 Promising Alternatives

#### HDD only during peak periods, where reasonably possible, and 80 km/h and/or 100 km/h; dynamic (throughput alternative)

#### 80 km/h everywhere 24/7 and HDD only where necessary (environment alternative)

### Amsterdam Ring Road

#### Only one section possible and necessary - southeast section

### HDD - Amsterdam Ring Road

#### Configuration of ring roads according to throughput and environment alternatives

##### Prediction traffic volumes

###### Vehicle hours of delay

###### Traffic safety

###### Air pollution

###### Noise

          - Cost-benefit analysis

#### Considerable hours of delay in the environment alternative - extra and unnecessary delay in the off-peak period when congestion doesn't exist

### Voorburg Weaving Area

#### HDD should be implemented

#### Because of 100% enforcement, motorists wait until an acceptable gap is available

#### Solutions to issues:

##### 1 - skip 80 km/h and/or enforcement

##### 2 - maintain 80 km/h, except for peak hours; then 100 km/h

## Vision on ring road management

### Ring roads have strategic position within the entire network

### No network if they were taken away or fully congested

### Ring roads

#### Keep traffic moving

#### Recognize/use connection with regional and local networks

#### Have control over in-flow traffic

#### Stimulate out-flow traffic

### Traffic Management Instruments

#### Variable speed limits

#### Overtaking prohibitions for heavy freight vehicles

#### Keep your lane?

#### Lane changing prohibitions

#### Dynamic access per lane for various purposes

#### Intensified incident management

### Infrastructural provisions

#### Flexible division of carriageway (dynamic lanes)

#### Narrow lanes

#### Access control

#### Exit control

#### Buffers

#### Electronic separation of traffic streams (i.e., through vs. local traffic)

### Equipment

#### Overhead lane signs

#### Full matrix message signs

#### DMS

#### Graphic DMS

#### Dynamic road markings

#### Cameras

## Human factors

### A lot of information on the roadway

### Inquiry into the understanding of the status of lanes

#### All vehicles

#### Trucks and/or buses only

#### Peak, plus

#### Buffer

#### HOV

#### HOT

#### Closed (i.e., if environmental reasons)

#### Breakdowns only

#### B-lane

#### Etc.

## Variable speed limits

### System automatically varies speed limits

### Speed limits with and without circle are both regulatory - understanding of those with flashers and no circle are still regulatory

### Only enforce when there are circles around the speed limit - Ministry of Justice determination

### Only when there is a speed drop are flashers used

## Access control

### Did a pilot test of the junction control on the A1 and it showed promising results

### Junction of ramp and provide priority access to the ramp and close a lane on the GP lanes

### Typical network management measure that has a collective gain

## Speed-flow relationship

### Where would the optimum location on the curve be to optimize the system?  1800? 2000?

### Increase chance of shockwaves the closer you move to the right on the curve

### Do you want more capacity over a short time or more reliability over most of the time

### Try to get a high reliability - more to the left on the graph - not at capacity - probably a v/c ration of 0.75 or 0.8 to provide breathing room

# Hard Shoulder Running (HSR) in the Netherlands

## Bert Helleman, Senior Consultant Smart Roads and ATMS

## Introduction and Background

### 1994 - policy to have a more efficient use of facilities

### 1995 - Traffic Management Program (1995-2000)

### 2003 - traffic management is usual business

### 2004-2007 - program ZSM (hard shoulder running) and regional traffic management (area approach) - visible, smart, and measurable

### Growth of congestion and bottlenecks

## Main Issues of ZSM Program

### Improve infrastructure (missing links in road network)

### Improve utilization (HSR, planning road works, IM)

### Improve procedures (emergency road widening act - enabled through legislation)

### Improve input from road users (periodic road user polls)

## 2004 - 2007 Program for ZSM

### 150 km of HSR and plus Lanes (in use) in country (dynamic cross section)

### 235 km of HSR and plus lanes (planned)

## Problems - EU regulations for air quality must be implemented into the country's air quality policy

### Implementation is a challenge

### Act still required

## 3 concepts

### HSR (hard should will be in operation during peak hours)

### Plus lane (variable left lane)

#### one smaller lane and standard lanes with a narrower RH hard shoulder and allows it to remain as an emergency lane

#### reduced speed limit

#### Can't really use the median because of existence of lighting and/or gantries for VSL

#### Trucks may only drive on the right-hand shoulder

### Flexroad (dynamic cross section) - would like to realize a fully dynamic cross-section and have 2 in off-peak and 3 in peak with dynamic pavement markings

## Design and Layout of HSR lanes

### Starting position = situation outside peak hours

#### Self-explaining standard Motorway cross-section

### Adoption of German solution

#### Special sign (provision of law)

#### Continuous marking line

#### Use of DMS-lane signs only during peak hours (and temporary in case of incidents)

#### ONLY use this in the peak period

#### Having a discussion about consistency in operations

#### Variable lane signs on gantries

#### Variable static signs (rotating drum on ground-mount signs)

### Variable route signing of HSR lane at exit

#### Shifted deceleration lane to the outside where it was formerly an emergency lane and the HSR goes over the gore

### Speeds are only posted after each entry to the motorway on ground-mounted static signs that will rotate the message

## A ride on the A50

### Initially HSR was only between junctions and didn’t go through junctions

## Who decides to implement HSR

### Daily:  there is a trigger in the TMC that depends on traffic flow >1500 vphpl - system will be switched on but not automatically - need to inspect the shoulders by the operator to ensure clearance

### HQ must decide to implement them -

#### regional division may not make the decision

#### Do an evaluation with models to see if there isn't a new problem after implementation and shifting of bottleneck downstream of the VSL

### A few will be in operation because of growing congestion for 6-8 hours a day

### Do it only as many hours as the traffic will justify operations because there is a safety tradeoff with the shoulders to alleviate congestion - not 24/7

## Reaction of stakeholders (fire brigade, police, EMS) was initially negative

### Obligation is to have communication with stakeholders and make a calamity / IM project effective

### As long as the traffic flows you can make the HSR free

## Public initially liked the idea

## Don't here very negative sounds from stakeholders and are waiting for the new ones to be delivered

## Have continuous cameras along the stretch of motor way

## Refuge areas put in every 1 km

### Relationship between distance to refuge areas and HSR speeds.

### Large increase in congestion if you don't use HSR as opposed to increase in congestion without shoulder for refuge

## Additional Facilities

### MTM system (overhead lane signs)

### ERA's (emergency refuge areas)

#### Average use 185 / 1,000,000 veh/km

#### Approx 90% used as a "parking place" (5% real break down

#### Great impact of distance3 between refuge areas

#### Very few accidents caused by breakdown vehicles but . . .

##### Great severity of accidents (2-3 times)

##### Particular at dawn/night conditions (70%)

### Speed reduction at times of HSR

### Variable route signs at junctions

### Advanced incident detection

### CCTV surveillance

### Incident management

### Public lighting

## HSR and Incident Management

### Safety prevention of (secondary) accidents

#### Fast protection of breakdown vehicles)

### Accessibility for emergency services

#### Fast clearing lanes

### Compromise between false

### History of loops every 75 m

### Expensive and many false alarms

### Currently

#### AID (proven system) and blockaded loop detector (optimizing - get more information about the gap shockwave moving in front of the incident rather than the vehicle shockwave moving behind the incident)

#### Mobile phones

## Innovative Instruments

### Dynamic road marking

## Research and Practice

### Lane occupation HSR

### Simple HSR lanes between two junctions

### New HSR lanes will go over junctions and are therefore more complex

## Monitoring and evaluation

### Quick scan on every new HSR project

### National evaluation of XSM-program

#### Accessibility

#### Safety

#### Evaluation of process

## HSR and Incident Management

### Spillback / tailback warning information on VSL - implemented automatically

### Red X implementation to close HSR for emergency access

### Flashers indicate congestion

### Gantry speed limits override those on the shoulder-mounted

### Size of indicators:  1 m X 1 m

## Only sign speed limits when they go down from the standard speed limit of 120 km/h

# Evaluation of Heavy Goods Vehicle Lanes on the A16

## Henk, Jansma, Senior Advisor Road Safety, Traffic Transport & Infrastructure, Public Works and Water Management Zuid-Holland

## Accessibility Mainport Rotterdam

### Intermodal approach

### Inland waterways, river Rhine

### Rail, Betuweroute

### Roads A15, A16, A20, A13, and A29

### Facilitation of freight transport by road

### Dedicated truck lanes and buses but not for private cars with a trailer

### HGV lanes on the A16 and A20

## Densely used roads around Rotterdam

## Dedicated lanes for trucks on a bridge on the A16 in the past

## Different scenarios for that on the A16 and A20

## Heavy Goods Vehicle Lanes

### A20 - Physically separated with concrete  barrier

#### Really a direct connect bypass

#### Safer that the A16 AGV lane

### A 16 - Not physically separated from traffic

#### 5 km in length

#### Dedicated lane on bridge across river

#### 50-70% of the trucks use the dedicated lane

#### Developed new sign - the best way to make a new traffic sign is to use something that already exists

#### There are people who abuse the lane for their own purposes

##### SU-trucks

##### Private vehicles

##### Difficult to catch them - enforce them

#### Upgrade is 4.5%

## Reasons to evaluate

### Road safety

#### Not many accidents on the HGV, but if there is one, it is typically a fatality

### Efficient use of lane

#### Doubts efficiency

### Effect of lane for trucks

#### Only a few minutes

#### Typically due to taking over cars by trucks at the right side

### Historically

#### Depends on what society wants for broader application

#### Doubts efficiency of lanes

### Speed differential may be of concern and of safety

### % truck traffic is probably around 8-16 %

### Distribution of truck traffic on transportation system

#### 45% - motorways

#### 45% - inland waterways

#### 10% - rail

### First results of Research

#### Road safety sub potential

#### Time profit for road haulers marginal

#### Traffic flow indifferent

#### Traffic picture inconsistent

#### Emergency lane doesn't exist on this section which may impact the safety of the lane

### Real policy considerations

#### Zero option, maintaining HGV lanes

#### Reset of original design, only two lanes

#### Original design together with a dedicated lane for all traffic during rush hour - technical and public policy problems with implementation

### Problem with missing emergency lanes

### Video